## Slide 1
EM modelling workflow
Write geometry description using GdfidL primitives
Specify the material mapping
Specify the port definitions
Specify the mesh definitions
<model name>_model_data
Generate STL files with geometry parameter files
Get a folder structure containing all the STL files for all values of the defined parameter sweeps
Generate overview reports for each parameter sweep
Blend_reports.m
run_models.m
Post process models
Results put into the report folder
Run models
Results put into the data folder
Make GdfidL input files
Write geometry description using FreeCAD primatives
Specify geometric parameter sweeps
<model_name>.py
Specify the mesh definitions
Mesh_definition.txt
Define the material of parts
Specify geometric parameter sweeps
Specify material parameter sweeps
Specify meshing parameter sweeps
<model name>.m
For each input file
Define the material mapping of each STL part
Define the order that the STL are loaded.
Define the material of parts
Specify the port definitions
Specify the geometry fractions to run (1, ½, ¼).
Specify material parameter sweeps
Specify meshing parameter sweeps
<model name>.m
Run on report folder data
Generate reports
generate_report.m
Analyse results
analyse_pp_data.m
On the modelling machine
Anywhere
For each model
Running <model_name>.m makes this happen.
These can be run on a separate machine. This has the advantage that you can look at results of earlier simulations before the full set has completed.
Also the modelling machine is only doing the EM simulation thus gets through the models faster.
Not currently used
This is now the EM CAD frontend project
Extract particular types of data for sets of models
extract_all_wlf.m

## Slide 2
EM modelling workflow – parameter optimisation
Run a series of short wake PEC models with different mesh densities.
This returns a series of geometric wake loss factors which identify the minimum mesh density required to have a stable wake loss factor.
Using the determined simulation parameters, run geometry /material sweeps
Take care if the geometry changes reduce gaps.
Run a lossy model
Identifies geometric + material losses
Gives good resolution wake loss spectra
Run a long wake PEC model
Identifies geometric losses
Gives good resolution wake loss spectra
Base model parameter setup
Determine the appropriate mesh density
get_wlf_vs_mesh_density.m
Determine the appropriate wake length
(wake length studies can be done in postprocessing)
Rename the results folder if you wish to keep the results.