## Slide 1
Workflow for model validation
(Getting the initial settings)
Run a series of short wake models with different mesh densities
Plot wake loss factor vs mesh density
get_wlf_vs_mesh_density.m
Pick the model where increasing the mesh density further does not influence the wake loss factor.
Using the selected model:
Plot decay level vs wake length
get_decay_level_vs_wake_length.m
Re assign the selected model as the new Base model
select_base_model.m
Set up your parameter sweeps as desired, and run
If you are validating an engineering model you are probably done
Generate report
Change the input file to reflect the new wake length settings
Change the input file to reflect the new mesh settings
Add longer wake length to the input file and run additional models
Pick the wake length where the wake potential has decayed sufficiently.