## Slide 1
EM modelling workflow
Generate STL files with geometry parameter files
Get a folder structure containing all the STL files for all values of the defined geometric parameter sweeps
[EM CAD frontend project]
Generate overview reports for each parameter sweep
Blend_reports({model})
postprocess
Results put into the report folder
simulate
Results put into the data folder
On the modelling machine
These can be run on a separate machine. This has the advantage that you can look at results of earlier simulations before the full set has completed.
Also the modelling machine is only doing the EM simulation thus gets through the models faster.
Specify the mesh definitions
Define the material mapping of each STL part
Define the order that the STL are loaded.
Define the base material of parts
Specify the port definitions
Specify the geometry fractions to run (1, ½, ¼).
<model name>.m
Define voltage monitors
Define field capture
Define the setup for each simulation type
Specify material parameter sweeps
Specify meshing parameter sweeps
Specify beam position sweeps
current_simulation({<model name>}, 'stages’, {<stage>}, 'sim_types’, {<types>})
Run on report folder data
Stage
wake
plot_data
analyse
plot_data
analyse
reconstruct
analyse
field_extraction
plot_data
plot_fields
sparameter
eigenmode
Stage
Write input file
types = 'geometry’, 'wake’, 'sparameter’, ‘eigenmode’

## Slide 2
EM modelling workflow – parameter optimisation
Run a series of short wake PEC models with different mesh densities.
This returns a series of geometric wake loss factors which identify the minimum mesh density required to have a stable wake loss factor.
Using the determined simulation parameters, run geometry /material sweeps
Take care if the geometry changes reduce gaps.
Run a lossy model
Identifies geometric + material losses
Gives good resolution wake loss spectra
Run a long wake PEC model
Identifies geometric losses
Gives good resolution wake loss spectra
Base model parameter setup
Determine the appropriate mesh density
get_wlf_vs_mesh_density.m
Determine the appropriate wake length
(wake length studies can be done in postprocessing)